## Slide 1: Ground rules
Sustainable
  Our PPTs default mode is dark. Energy saved in every slide. Navigate through the bright cover slides and use the Knowit-black-background for everything else.
Accessible
  Our columns are narrow and line lengths short for an easy, and accessible read
Keep it simple
  Highlight only what strengthens your story. Leave everything else behind. And make every illustration count 

## Slide 2: Visual prioritization

## Slide 3: PowerPoint skills
Tips
  Our template contains 38 different layouts, choose with care (and ask a colleague if you can’t find them)
  The layout names might be helpful
  Confused about colors or typographic rules? Check out the margins for some guidance
  Have fun! (Break some rules if it helps you elevate your kick-ass-content)

## Slide 5: Embedded academy Communication interfaces

## Slide 6: Content
Introduction
SPI
UART
I2C
Jtag
Other topics

## Slide 7: Lab
Introduction
In today’s lab we will implement a small uart interface to communicate with a PC-program

## Slide 8: Notes from previous session

## Slide 9: Reminder for today
Notes from last session
Stack
Flash

## Slide 10: SPI

## Slide 11: SPI
SPI
Serial peripheral interface
Used for short distance communication between integrated circuits
Master-slave configuration
Commonly used for flash, DAC, Eeprom etc.

## Slide 12: How it works
SPI
Every clock cycle, main and sub shifts out one bit and reads one bit.
After 8 cycles one byte is transmitted

## Slide 13: How it works
SPI

## Slide 14: Pros and cons
SPI
Cons
  Only handles short distances
  No formal protocol
  No interrupts
  No flow control
  No acknowledgement
  No error check
Pros
  Good signal integrity
  High throughput
  Full duplex (both can transmit and receive simultaneously)
  Simple hardware
  Low power

## Slide 15: I2C

## Slide 16: I2C
I2C
Inter-integrated circuit
Used for short distance communication between integrated circuits
Master-slave configuration
Commonly used for Eeprom, real-time clocks, simple LCDs
System Management Bus (SMBus) defines stricter substandard
Typically 100 kbit/s

## Slide 17: How it works
I2C
Starts by pulling SDA low while SCL is high
Sends address to node to communicate with
Send data 8 bits at a time until stop
Ack on every byte

## Slide 18: Pros and cons
I2C
Cons
  Slow
  Address conflicts
  Requires more space on PCB
Pros
  Cheap
  Require only two pins to control a full network
  Semi duplex
  Addressing
  Acknowledgements

## Slide 19: UART

## Slide 20: UART
UART
Universal Asynchronous Reciever-Transmitter
USART also exist which support synchronous communication
Used for serial communication
Also known as RS232

## Slide 21: How it works
UART
Requires same configuration on both ends for:
  Voltage (can be solved with level switch)
  Baudrate
  Parity bit
  Data bits size
  Stop bits size
  Flow control

## Slide 22: Pros and cons
Uart
Cons
  Only allows two devices on bus
  Low speed
Pros
  Simple
  No clock signal requirement
  Error detection
  Supports longer distances

## Slide 23: Jtag

## Slide 24: JTAG
JTAG
Joint Test Action Group
Industry standard for verifying electronics
Used for debugging embedded systems
Dedicated debug port
Direct access to system addresses and data buses
Test Access Port (TAP) is a key element
Serial Wire Debug (SWD) is a two pin alternative, defined for ARM architecture

## Slide 25: How it works
JTAG
TDI (Test Data Input) — test data input. The commands and data are inserted into the chip through this pin on the rising edge of the signal TCK.
TDO (Test Data Output) — serial data output. Commands and data are output from the chip through this pin on the falling edge of the signal TCK.
TCK (Test Clock) — clock input.
TMS (Test Mode Select) — controls the transitions between states of the finite state machine TAP.
TRST (Test Reset) — reset signal of the TAP finite state machine.

## Slide 26: Other protocols

## Slide 27: Other protocols
Other protocols
Controller Area Network (CAN)
Modbus
Ethernet/IP
EtherCAT

## Slide 28: Other topics related to the course?

## Slide 29: DMA Clarification
I2C
Direct Memory access allows a peripheral device to write straight to memory
DMA request from peripheral
DMA Controller provides bus access to memory
DMA Controller sends interrupt to processor when data transfer is done

## Slide 30: Questions?

## Slide 31: Lab part

## Slide 32: Our icons

## Slide 33: UN SDG (PNG)

## Slide 34: UN SDG (SVG)