## Slide 1: Ground rules
Sustainable
  Our PPTs default mode is dark. Energy saved in every slide. Navigate through the bright cover slides and use the Knowit-black-background for everything else.
Accessible
  Our columns are narrow and line lengths short for an easy, and accessible read
Keep it simple
  Highlight only what strengthens your story. Leave everything else behind. And make every illustration count 

## Slide 2: Visual prioritization

## Slide 3: PowerPoint skills
Tips
  Our template contains 38 different layouts, choose with care (and ask a colleague if you can’t find them)
  The layout names might be helpful
  Confused about colors or typographic rules? Check out the margins for some guidance
  Have fun! (Break some rules if it helps you elevate your kick-ass-content)

## Slide 5: Embedded academy

## Slide 6: Who am I?
33 years old
Studied engineering physics at Chalmers
Started at Box of Energy, startup in Gothenburg
Previously four years at Aros electronics
Working at Knowit since May 2022 with engcon

## Slide 7: Course overview
Course overview
Four Tuesdays 16.00-20.00
Tuesday 12th November: Introduction
Tuesday 19th November: Assembler and compilers
Tuesday 26th November: Electronics and HW interfaces
Tuesday 3rd December: Communication interfaces
Every session will be around 2 hours of lecture and 2 hours of lab, related to the content in the lecture
Resources available on Github, feel free to play around and test things on your own
Reach out if you have any questions or have hard time understanding some concepts
Disclaimer! Use this course as advisory information. Adapt what you learn to your context and look up details as needed.

## Slide 8: Course content
Course overview
Tuesday 12th November: Introduction
  Processor components
  Processor manual
  Hex and binary numbers
  Memory types (flash, ram, stack, heap etc)
  RTOS (semaphores, threading, FreeRTOS)
Tuesday 19th November: Assembler and compilers
  Arm assembler
  Compiler flags
  Testing assembler code
  Debugging
  Map and list files
Tuesday 26th November: Electronics and HW interfaces
  Processor manual, deep dive
  DAC and ADCs
  Timers and Interrupts
  Voltage dividers
  Level switches
  Measurement
Tuesday 3rd December: Communication interfaces
  SPI
  UART
  I2C
  J-tag
  Other topics

## Slide 9: Lab
Course overview
Approximately two hours every session will be dedicated to a lab related to the lectures
Labs will be performed on a STM32 Nucleo-64 development board with peripherals
Dev boards are available on all sites with participants, please share them among each other
During the course we will implement drivers, write assembler code and play with peripherals
Requires STM32CubeIDE for easy target compilation and debugging
Collaboraion is encouraged, help eachother and discuss solutions with eachother

## Slide 10: Embedded academy Introduction

## Slide 11: Content
Introduction
What is embedded?
Processor components
Processor manual (first look)
Memory types
Real-Time Operating System (RTOS)
Hex and binary numbers

## Slide 12: Lab
Introduction
This week the lab will let us get to know the IDE, some basic interfaces and show us how to debug on the board.
It will also involve getting to know a RTOS and setting up threads.
The end goal is to blink a led on the board using FreeRTOS, both using a timer and pushing a button.

## Slide 13: What is embedded?

## Slide 14: Definition
What is embedded?
Not very well defined. Qt states the following which I felt summarize the general opinion quite well
An embedded programming language is a programming language that developers use in embedded systems. In general, the languages offer low-level access to the device hardware. Developers use several common programming languages for embedded systems.

## Slide 15: Differences from other types of programming
What is embedded?
Specialized for certain hardware
Real time requirements
Limited resources
Demanding test and validation
Minimalistic user interface
Safety can have other aspects

## Slide 16: Examples
What is embedded?

## Slide 17: Processor components

## Slide 18: Overview
Processor components
STM32F302x6/8

## Slide 19: Common components - CPU
Processor components

## Slide 20: Common components - Peripherals
Processor components
DAC
ADC
Timer
CCU
RTC
Watchdog
POSIF
PWM
Communication interfaces (SPI/I2C/UART/CAN)

## Slide 21: Processor manual

## Slide 22: Overview
Processor manual

## Slide 23: Overview
Processor manual
Lot of information in manual
Usually good help from Application Notes

## Slide 24: Memory types

## Slide 25: Memory types Overview
Memory types
Flash
RAM
EEPROM
Stack
Heap

## Slide 26: Flash
Memory types
Non-volatile (stays the same after reboot)
Read only (with exceptions)
Contains op codes (basically your code)
Could also be external storage
Limited number of erases possible
Slow
Use const to force variables to be stored in flash

## Slide 27: RAM
Memory types
Volatile (will be cleared on reset)
Fast
Read and write
Basically unlimited writes
This is where global variables are stored
Use static to place variables here

## Slide 28: Eeprom
Memory types
Electrically Erasable Programmable Read Only Memory
Non-volatile memory
Handles more writes
Quite slow
Usually used for storing parameters which needs to be changed during runtime and stored between restarts
Could be replaced by FRAM for faster reads

## Slide 29: Stack
Memory types
Software implementation
Stored in RAM
LIFO
If too small, an overflow could cause a lot of undefined and hard to debug errors
This is where function variables are stored

## Slide 30: Heap
Memory types
Dynamically allocated memory.
Achieved with stdlib-function such as malloc() and free()
Usually avoided in embedded C, dynamic memory allocation is quite dangerous and need to be safe

## Slide 31: Real-Time operating system

## Slide 32: Purpose
Real-Time operating system
Semaphores
Scheduler
Threading

## Slide 33: Concepts
Real-Time operating system
Semaphores
Scheduler
Threading

## Slide 34: Implementations
Real-Time operating system
FreeRTOS
SafeRTOS
Embedded Linux

## Slide 35: Implementations
Real-Time operating system
FreeRTOS
SafeRTOS
Embedded Linux

## Slide 36: Hex and binary numbers

## Slide 37: Binary numbers
Hex and binary numbers
Processor only uses 0 and 1, thus all numbers a stored in binary
Binary is simply base two, rather than base 10 as the decimal system
Indicated with 0b when coding
128 + 64 + 0 + 0 + 8 + 0 + 2 + 0 = 202

## Slide 38: Hex numbers
Hex and binary numbers
Hexadecimal numbers are commonly used in embedded programming
Uses base 16 and lets A = 10, B = 11, C = 12, D = 13, E = 14 and F = 15
Indicated with 0x when coding
Two hex numbers corresponds to one byte or eight bits

## Slide 39: Correlation between hex and binary numbers
Hex and binary numbers
One hex digit matches four binary digits
Easy to convert between hex and binary
More dense with hex format
Useful for bitmasks for example
Commonly used when interacting with processor registers

## Slide 40: Questions?

## Slide 41: Lab part

## Slide 42: Our icons

## Slide 43: UN SDG (PNG)

## Slide 44: UN SDG (SVG)