## Slide 1: Ground rules
Sustainable
  Our PPTs default mode is dark. Energy saved in every slide. Navigate through the bright cover slides and use the Knowit-black-background for everything else.
Accessible
  Our columns are narrow and line lengths short for an easy, and accessible read
Keep it simple
  Highlight only what strengthens your story. Leave everything else behind. And make every illustration count 

## Slide 2: Visual prioritization

## Slide 3: PowerPoint skills
Tips
  Our template contains 38 different layouts, choose with care (and ask a colleague if you can’t find them)
  The layout names might be helpful
  Confused about colors or typographic rules? Check out the margins for some guidance
  Have fun! (Break some rules if it helps you elevate your kick-ass-content)

## Slide 5: Embedded academy Assembler and compilers

## Slide 6: Content
Introduction
ARM assembler
Compiler flags
Testing assembler code
Debugging
Map and list files

## Slide 7: Lab
Introduction
Implement assembler function

## Slide 8: Notes from previous session

## Slide 9: Reminder for today
Notes from last session
Stack
Flash
RAM

## Slide 10: ARM assembler

## Slide 11: What is assembler?
ARM assembler
Low level code, close to machine code
Different kinds of assembler depending on processor architecture
ARM, x86 and x86-64 most common architectures
ARM mainly used in embedded systems
Different kinds of ARM instruction sets

## Slide 12: Processor registers
ARM Assembler
Rm, general registers
SP, stack pointer
LR, link register
PC, program counter

## Slide 13: Assembly instructions
ARM Assembler
ADD adds registers or values
  ADD r1, r2, r3 means r1 := r2 + r3
SUB subtracts registers
  SUB r1, r2, r3 means r1 := r2 – r3
MOV copies a value to a register
  MOV r1, r2 means r1 := r2
MUL, DIV multiplies and divides respectively
AND performs bitwise and
OR performs bitwise or
ASR performs an arithmetic shift right
LSR performs a logical shift right

## Slide 14: Assembly instructions
ARM Assembler
STR stores a register at a memory address
  STR r1, [r7, #8] stores the value of r1 at the memory location of r7+8, RAM[r7+8] := r1
LDR load value from a memory address
  LDR r1, [r7, #8] loads the value from memory of r7+8 into r1 r1 := RAM[r7+8]
CMP compares two values, subtracts two values and discards the result but update NZCV-flags
  CMP r1, r2 performs r2-r1 and sets flags accordingly. If they are equal Z is set two one, if r1 is larger than r2 N is set to 1
B branches, or jumps, to labled PC-relative address
  B .function will jump the program counter to the where .function is stored in memory
  BX lr will change the program counter to the address stored in lr, normally a return.
PUSH stores a register value to the stack and updates the stack pointer
POP loads a register value from the stack and updates the stack pointer

## Slide 15: Condition code suffixes
ARM Assembler
Can be added as a suffix to most instructions
Will look at the NZCV registers from previous operation to evaluate condition
EQ equals
NE not equal
GE signed greater or equal
LS unsigned lower or same
CMP r1, r2 compares r1 and r2
BLE _jump branches to _jump if the value in r1 is signed less than or equal to the value in r2

## Slide 16: Examples
ARM Assembler
Assembler code can be written directly in C with the asm() function
The asm()-block can take inputs and outputs to interact with C code

## Slide 17: Map and list files

## Slide 18: Map files
Map and list files
Contains static symbols and their address
Produced by the linker
Contents can be controlled with a linker script
Useful for error originating from RAM

## Slide 19: Map file sections
Map and list files
.text, contains instructions located in flash
.rodata, contains constants located in flash
.data, contains initialized variable, copied from flash to RAM during startup
.bss, contains uninitialized variables, stored in RAM, often (but not guaranteed) initialized to 0

## Slide 20: List files
Map and list files
Contains assembly code and its address
Often C-code in between for clarity
Can also contain error and warning messages
Might also be used to determine memory and stack usage

## Slide 21: Debugging

## Slide 22: Debugging C
Debugging
Debugging C code is usually difficult
Hard crashes often only return an address where the crash occurs
Map and list files useful
Debugging tools available to step through the software

## Slide 23: Debugging real-time systems
Debugging
Debugging real-time systems is usually difficult
Hard to use debugging tools to step through code
Work around by modifying code and using potential user interfaces for printouts

## Slide 24: Testing assembler code

## Slide 25: Testing on hardware
Testing assembler code
Instruction stepping mode lets you step through assembly code
Disassembly usually available
Possible to change register values to change behaviour of code

## Slide 26: Testing on computer
Testing assembler code
Usually running on x86 architecture and code is compiled for ARM
QEMU lets us emulate ARM architecture
gdb-multiarch can be used to check registers and step through arm code without hardware
Lots of other tools available

## Slide 27: Compiler flags

## Slide 28: Compiler flags
Compiler flags
Lots of different flags, both for gcc and for ld
Optimization
  Ranges from –O0 to –O3 and some other special versions such as –Os
  Higher number increases compile time and performance of code
  Higher number makes debugging harder
  -O0 is default and useful when debugging
  -Os is –O2 but optimized for size, common in production
Debug
  -g sets debug level when using gdb
  -g0 is nu debug information and –g3 is maximum.
  –g will use level 2, default debug information
Generate map and list files
  -Wl,-Map=output.map will generate a map file
  objdump responsible for generating list file
  objdump –h –S output.elf > “output.list”

## Slide 29: Questions?

## Slide 30: Lab part

## Slide 31: Our icons

## Slide 32: UN SDG (PNG)

## Slide 33: UN SDG (SVG)